Bioengineering
Introduction to Physiological Measurement
Transducers and Instrumentation for Physiological Measurement

---
Outline
- General Principles of measurement
- Examples of measurement
- Sensors for measurement
- Unobtrusive measurement: non-invasive

---
Why Measure?
- To define normal physiology
- To classify deviations from normal physiology – i.e., pathophysiology
- To understand processes and systems
  N.B. Physiology is the study of processes and systems that enable homeostasis

---
The Measurement Process

---
Examples of Measurement
- Measurement of chemical and gas concentrations
- Measurement of structure - imaging
- Electrophysiological Measurement
- Cardiovascular Fluid Mechanics Measurement
- Musculoskeletal Mechanical Measurement

---
Biopotential Measurement – ECG and Nerve Activity

---
Concepts for Measurement
- A signal is a physical quantity – typically it varies with time (but it can vary with length, space, etc.)
- A system is a process that can modify a signal

---
Transduction of Signals
- Transducer converts one kind of physical energy into another form
  - e.g., pressure to resistance, temperature to voltage
- Therefore, a transducer is also a system that modifies the signal

---
Characteristics of signals
- Steady state value – single value measurement, slow measurement
- Transient measurement – time-varying measurement

---
Characteristics of Systems
- Predictable behaviour – i.e., stationary over time
- Linear – acts the same way on small signals and as well as larger signals

---
Review Questions
In each of the following transducers, what is the input and output?
  1. Manometer
  2. Weighing scale
  3. Load cell
  4. Accelerometer
1. A piston in a cylinder (like a syringe), and a displacement sensor, can be used as a pressure sensor. What are the potential difficulties with this arrangement? Is any additional element to be added? What is the zero reading of such a transducer?
2. When is an electrical pressure transducer better than a mercury manometer?

---
Characterization of measurement systems
- Static calibration
- Dynamic calibration

---
Static calibration of transducers
- Input-output relationship
- Linearity
  - Linear: y = m x+c
  - Compensating for non-linearity
- Offset
- Calibration and curve fitting

---
Dynamic calibration
- Transient behaviour of physiological systems
  - Changes in system output with time
- Dynamic response = response of a transducer or recording system to a changing signal
- Dynamic characterization
  - Time constant
  - Step response
  - Frequency response
  - Transfer function

---
Dynamic Measurement – Intra Arterial Blood Pressure

---
Digitization of Signals
- Sampling and Quantization
- Analog-to-Digital Converters
- The Sampling Theorem
  - If the signal is sampled at a rate which is at least twice the highest frequency contained in the signal, then the original signal can always be recovered

---
Characterizing signals
- Decomposing signals
- Identifying contamination of signals
- ---> Next lecture