Analog Processing of Signals
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Outline
Sensors for physiological data
Amplification, linearity, offset
Concepts of Filtering
Frequency filtering
Frequency content of signals
Conclusions

---
Transducers for Physiological Signals
- Mechanical measurement
  - Strain gauges and bridge measurement
  - Piezoelectric sensors
  - Electromagnetic sensors
- Electrophysiological measurement
  - Biopotential electrodes
- Displacement or length measurement
  - Camera based measurement
  - Resistive, capacitive, inductive sensors
- Optical measurement
  - Spectral measurement - spectrophotometry
- Actuators
  - Electromagnetic actuators
  - Piezoelectric actuators

---
Measurement System - I

---
Particle Filtering by Size

---
Filtered Particle Size Distribution
- Driving forces:
  P1-P2, and P1-P3
- Separation is not perfect, some small particles miss the filter
- Quality of filtering depends on filter pore size accuracy and driving forces
- Filter is described by:
  - Pore size (size threshold)
  - Small-pass or Large-pass

---
Combination of filters I – cascading filters

---
Combination of filters II – adding filters

---
Summary of Particle-Size Filter
- Size filtering is imperfect, but can be improved by using multiple screens one after the other (cascade)
- Combinations of filters can be used to produce complex size filtering. The basic combinations are:
  - Cascading: this is equivalent to multiplying size distribution function
  - Adding: this is equivalent to adding size distribution function
- Filtering quality depends on accuracy of pore-size and pressure differences
  - Pressure differences can be controlled using fluid pumps

---
The use of analogies
- Analogies are useful to extend intuition to an unusual or unaccustomed situation
- Analogies are imperfect
- The particle filter analogy has some important limitations
  - The temporal and spatial relation between particles is not preserved during flow
  - In the case of most time signals in physiology, the temporal relation between components of the signal is very important

---
Electrical Filters – the basic RC filter

---
Filtered Signal Frequency Distribution
- Cutoff frequency:
  Cutoff freq is half-power freq, or -3dB freq
- Separation is not perfect, there is a transition region
- Quality of filtering depends on source current, load currents. These depend on source impedance and load impedances
- Quality of filtering can be improved using active components
f_o =1 over { 2 %pi RC}

---
Summary of Frequency Filtering
- Frequency filtering is imperfect, but can be improved by using multiple filters one after the other (cascade)
- Combinations of filters can be used to produce complex frequency filtering. Basic combinations are:
  - Cascading: this is equivalent to multiplying frequency distrbution functions
  - Adding: this is equivalent to adding frequency distrbution functions
- Filtering quality depends on accuracy of resistor & capacitor values and source and load impedances
- Using active components (transistors, integrated circuits), the effect of source and load impedances can be greatly reduced

---
Frequency content of a time-varying signal
- Preface: Any composite fluid (like blood) can be regarded as a mixture of particles of different sizes
- Any composite signal (any general time varying signal) can be regarded as a mixture of pure frequencies
  [Note: Here, “pure frequency” means a signal whose shape doesn't change with differentiation or integration. Sines and cosines (sinusoids) are such functions]
- Fourier decomposition is a mathematical process of identifying the component frequencies in a signal

---
Basic Filter Characteristics
- The basic RC filter is a first order filter (described by a first order differential equation)
- Cascading two filters will result in multiplication of the frequency selectivity. This makes a second order filter.
- Adding two filters in parallel will add the frequency selectivity. This usually results in a 2nd order system.
- The basic filter types are:
  - Low-pass filter
  - High-pass filter
  - Bandpass filter
    - cascade HPF (fH) and LPF (fL), with fH< fL
  - Bandstop filter
    - add LPF (fL) and HPF (fH), with fL< fH

---
What is frequency analysis of signals and systems
- Fourier series: Any periodic signal can be described by a set of sine waves
- Fourier transform: Any arbitrary signal can be described by a continuum of sine waves
- Illustration: simulation from Signals & Systems book
- Freq spectrum=Freq distribution of signal power
- Freq response=Freq distribution of system response

---
Frequency distribution graphs
- Linear plots – linear frequency and linear amplitude
  - Graphs are complex curves
  - Combining graphs is tedious
- Log-Log plots – logarithm of frequency and logarithm
  - Graphs can be approximated by a few straight lines
  - Combining graphs is easy – can usually be added
  - Log of frequency – shows small frequencies with high resolution and high frequencies with large range

---
More complex filters
- Filters can be combined by cascading or addition to make more complex filters
- Higher order filters
  - Better stopping of unwanted frequencies
  - Transition region between passband and stopband can be designed
    - Butterworth, Bessel, Chebyshev, Elliptic, etc.
- Higher order filters can be unstable – producing artificial oscillations

---
Part II ...
Noise Removal

---
What is “noise”?
- Contamination by unwanted signals
  - Usually of external origin
  - Could also be of biological origin
- Noise can be periodic or it can be random
  - Electrical mains – caveat: SMPS
  - Radio waves, thermal noise

---
Filtering Noise

---
Frequency composition of Signal
- Every signal can be described in terms of a set of sinusoids
- Conversely, any signal can be constructed from a suitable set of sinusoids
- This is the Fourier Transform

---
Fourier Decomposition

---
Spectrum Analysis

---
Filtering: 1st and 2nd Order filters

---
How to select the cutoff freq: The Optimal Filter

---
The Optimal Filter
- Keep as much of the signal as possible
- Remove as much of the signal as possible
- Decide on a compromise between these two

---
Other Techniques
- Noise removal:
  - Ensemble Averaging
  - Adaptive filtering
- Signal Decomposition
  - Wavelet transforms