Analog Processing
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Amplifiers
- Frequency filtering
- Filter Characteristics – Gain and Phase
- Phase Distortion in Biological Signals
- Offline Filtering

---
Measurement schematic

---
Considerations in Designing Sub-systems (i.e.,Transducers, Amplifiers, Filters)
- The subsystem must draw very little power from the preceding subsystem
  - In the case of voltage signals, the subsystem must draw as little current as possible
  - This means the input impedance must be very high
- The subsystem must be capable of delivering as much power as the following or next subsystem requires
  - In the case of voltage signals, the subsystem must be able to deliver as much current as required
  - This means the output impedance must be very small

---
Thevenin and Norton equivalent for any voltage or current source
- Any voltage or current source can be represented by:
  - A perfect voltage source with a series impedance
    - (Thevenin equivalent)
  - A perfect current source with a shunt impedance
    - (Norton equivalent)

---
Attenuators and Amplifiers

---
Difference or Differential Amplifier

---
Operational Amplifiers
- Amplifier with differential inputs suitable for feedback circuits
- Very high gain
- Very high input impedance
- Low output impedance

---
Feedback Control System
{Y( s )} over { X(s) } = { G(s) } over { 1+G(s)H(s) }

---
Basic Amplifier with Adjustable Gain
{V_o} over { V_i } = A over { 1+A.{R_1 / (R_1+R_2) }} newline ~~~~~~~~= 1 over { 1/A + R_1/(R_1+R_2) } newline ~~~~~~~~approx 1+R_2 over R_1 ~~~~as A-> infinity

---
Simple Analysis of Op-Amp Circuits
- Due to high input impedance the current into amplifier at the two inputs is zero
- From the above point, the effective potential difference between the two inputs is zero (“virtually connected” or concept of “virtual ground”)
- The output is: Vo=(Va-Vb)G, with G→ very large

---
Inverting Amplifier
{ V_o } over { V_i } = - { R_2 } over { R_1 }

---
Differential Amplifier

---
Low-Pass Filter
{V_o (s)} over { V_i (s) } = - { R_2 ~ lline ` rline ~ C } over { R_1 } = - {R_2/R_1 } over { 1+R_2 Cs }

---
Signal contaminated by
noise distinctly separated in frequency

---
Lowpass filtering of distinct high frequency noise

---
Signal contaminated by
noise overlapping in frequency

---
Filtering Overlapping Noise

---
Optimal Filter - I
- Keep as much of the signal as possible
- Remove as much of the noise as possible
- This means:
  - In the frequencies where the signal and noise overlap, the filter attenuation is proportional to the ratio of signal to noise
  - In the frequencies where they don't overlap, keep all the signal and remove all the noise

---
Optimal Filter - II
- Consider the EMG and ECG both of which can be picked up simultaneously by electrodes on the chest
  - ECG spectrum: 0.05Hz-80Hz
  - EMG spectrum: 15Hz-300Hz

---
Cascading Filters
- The Laplace Transform converts the input-output relation in simple algebraic terms – i.e., only multiplications and divisions
- Multiple filters can be cascaded, and the cumulative effect is a multiplication of the individual input-output relations

---
Real Filters
- Real-time and offline filtering
- Implementation
  - Physical filters/Electrical – online/realtime
- Physical filters and online filters
  - Causal , cannot use future data
  - Have finite phase shift or time lag
- Offline filters (Digital Filters)
  - Can use “virtual future” data that has been stored

---
Phase shift in filters
- Phase shift can disrupt time relations in waveforms
- Phase shift can introduce lag between synchronous signals
- Linear phase filters introduce constant time lag to all frequencies
"Time lag:" %tau = %phi over %omega ~~~"where" %phi "is the phase shift and" %omega "is the frequency"

---
Characterizing Filters
- Frequency response
- Step response