Voice Coil Actuator
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Magnetic Circuits
- Voice Coil

---
Force Actuators - Electromagnetic actuator
- EMF in a coil
- EMF in a moving conductor
- Force on a conductor
- Magnetomotive force
V=-N {d %phi} over {dt}
V=-B u l
F=B`I`l
M=N`I

---
Magnetic Circuit equivalent

---
Field-Flux characteristics of a permanent magnet
- Permanent magnets BrHC =figure of merit (is large)
  - Steel, Ferrite: BrHC=9
  - Alnico: BrHC = 62400
  - Ne-Fe-B: BrHC=240000
- For electromagnets hysteresis (BrHC) should be small

---
Magnetic circuits
R_m = M_m over %phi = {H_c l_m} over {B_m A_m}
R_m = M_m over %phi = {N I} over {B_m A_m}
R_g = 1 over %mu_o l_g over A_g
%phi = M_m over {R_m + R_g} cdot R_g

---
Voice coil - actuator

---
Magnetic circuit of voice coil
R_m = H_c over B_r l_m over A_m
- Reluctance of magnet
- Reluctance of pole piece
- Reluctance of air gap
- Flux in air gap
- Flux density in air gap
R_p = 1 over %mu l_p over A_p
A_p = %pi d_1 ^2
R_g = 1 over %mu_o l_g over A_g
A_g = %pi d_g h_g
%phi _g = {H_c l_m} over {R_m + R_p + R_g}
B_g = %phi_g over A_g = {H_c l_m} over {R_m+R_p+R_g} 1 over A_g

---
Force developed by the voice coil
- Force on the coil
- Laplace transform
- Length of conductor in coil
F(t)=B_g cdot I_c(t) cdot l_c
F(s)=B_g cdot l_c cdot I_c(s)
l_c = %pi d_g N

---
Electrical Excitation of voice coil
- Excitation voltage
- Back emf due to movement
- Total Applied Voltage
V_e (s)=I(s)`Z_e (s)
V_b (s)=B_g l_c u(s)
V(s) = V_e(s) + V_b (s) newline ~~~~~~~~~~= {I(s)} {Z_e(s)} + B_g l_c u(s)

---
Electrical Equivalent
F(t) = m dot u(t) + k_b u(t) + k_1 int u(t) dt newline u(s) = F(s)/[ms+k_b +k_1 /s] newline u(s) = {B_g l_c I(s)} over{ms+k_b +k_1 /s}
V(s) = V_e(s) + V_b (s)= {I(s)} {Z_e(s)} + I(s) {B_g ^2 l_c ^2} over {ms + k_b + k_1/s}

---
Equivalent Electrical Impedance due to mechanical components
{V_b(s)} over {I(s)}~=~-B_g ^2`l_c ^2`{Z_m(s)}

---
Using a transformer representation
V_2 = k V_1 ~,~~~~~I_2=I_1 over k ~,~~~~V_2 over I_2 = k^2 V_1 over I_1 ~,~~~Z_L=V_2 over I_2 ~,~~~V_1 over I_1 = Z_L over k^2

---
Servo Motor

---
Application of Servo motor in Haptics

---
Haptics – Feeling in Medical Devices

---
End of Lecture