Ultrasound Measurement
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Piezoelectric as sensors and actuators
- Applications

---
Ultrasound Reflection Measurement

---
Ultrasound Instruments
%tau = 2d over c
- Time of echo:
- Attenuation:
- Automatic depth dependent gain compensation
%tau~ = ~2d over c
I_r over I_o~=~e^{- %mu (2d) }

---
Flow measurement
Transit time =
distance / (effective velocity in medium)

---
A-scan
- Plot time of reflected waves
- Depth dependent gain compensation is applied
- Calculate distance of every reflecting boundary

---
M-scan
- Repeated transmit-receive cycles
- Plot calculated distance for each cycle

---
B-scan
- Move position of the transducer
- Calculate depth of multiple reflections
- Plot depth as intensity on a 2D spatial display

---
Doppler shift
- Source frequency fo
- Source-target velocity u
- Propagation in medium with velocity c
- Dopplet shift fd
{ f_d } over { f_o } = u over c

---
Doppler flowmetry
- Ultrasound
  - Doppler measurement of motion

---
Doppler imaging

---
End of Lecture