Volume Measurement
and
Concentration Measurement
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Volume –
  - Electrical Impedance
  - Optical Absorption
- Optical density measurement
  - Absorption by chemicals
- Characteristics of Spatial Sensors
  - Spatial Transmission/Reception Pattern
- Chromatic measurement - spectrometry
  - Electrical
  - Optical
- Spectrophotometric oximetry

---
Electrical Impedance Plethysmography
%DELTA Z_b = { %rho_b L } over { %DELTA A} newline newline %DELTA V = L %DELTA A = { %rho _b L^2 } over { %DELTA Z_b }

---
Impedance Measurement – 2 electrode, 4 electrode
- Constant current source
- Voltage measurement across electrodes
- 2 electrode method
  - Electrode-tissue impedance is included
- 4 electrode method
  - Inject current across outer 2 electrodes
  - Measure voltage across inner 2 electrodes
  - If amplifier has high input impedance
    - Electrode impedance is excluded

---
Optical Emitters, Filters, Detectors
- Intensity is a function of frequency
  - Spectrum
- Spatial radiation, reception pattern
  - Angle dependent
  - Lenses and collimators
- Light transmission:
  - Incident energy = Transmitted+Scattered/reflected
- Transmission through multiple media
  - Snell’s law:
n_1 sin %theta_1 = n_2 sin %theta _2

---
Spectral characterisitics of Photodiode (SFH2270)

---
Directional Characteristics

---
Spectrophotometry for Blood Oximetry

---
Electrical Impedance Spectrometry

---
End of Lecture