Digital Sensors:
Digitization &
Data Communication
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Digital Sensors
- Digitization
- Numerical data representation
- Data transfer
- Packet data
- Wireless and network data transfer
- Digital to Analog - Pulse width modulation (PWM)

---
Digital Temperature sensor - TMP100

---
TMP100 – Data format

---
MAX30100 – Photoplethysmograph Sensor

---
MAX30100 - IC

---
Inertial Motion Sensor - MPU9250

---
Digitization

---
Sampling Theorem
If a signal is sampled at a rate of at least twice the highest frequency contained in the signal, then the original signal can be reconstructed from the samples.

---
Reconstruction of original signal from the samples
- The original signal contains frequencies less than half the sampling rate.
- If the sampled signal is low-pass filtered with a cutoff of exactly half of the sampling rate, then the original signal will be recovered.
- Practically, this method is difficult and expensive
- Approximate methods:
  - Zero-order hold
  - First order interpolation
  - Analog low-pass filter

---
Digitization and Quantization

---
Quantization “Noise”

---
Number representation
- Straight binary – only positive numbers
- For both positive and negative numbers
  - First half of numbers → same as straight binary
  - Second half → negative numbers
- Floating point numbers
  - Significand (fraction) and exponent

---
Parallel Data Transfer
- One wire per bit
- Plus ground wire
- Data updated when available
- Data read when desired

---
Serial Data Transfer
- Sequential transfer of bits
  - Big endian, little endian
- Synchronous
  - Requires a separate clock line
  - Clock rate determined by one Master clock
- Asynchronous
  - Each devices has Independent clocks
  - Clock rate needs to be same on all devices

---
Data lines – electrical connection
- Low voltage and high voltage data lines
- Ground referenced data line
- Differential data lines
  - USB, CAN
  - Immunity to electrical noise

---
Individual Bytes versus Packet data transfer
- Individual bytes
  - Simple universal protocol
  - Well established standard
- Packet data
  - Packet contains header and data
  - Header can contain source and destination information, other information
- Packet identifier and delimiters
  - Start of packet
  - Packet length

---
Network and wireless data transfer
- Network topologies
- Formation of networks
- Packet data transfer

---
Network Topology
- Network topologies
  - Star
  - Peer-to-peer
  - Mesh
- Co-ordinator devices
  - Terminal node Input/Output devices

---
Example wireless network
- IEEE 802.15 for Wireless Personal Area Networks - ad hoc networks
- Frequency band is 2.4GHz, 16 channels (channels 11-26), license free.
- Uses carrier sense multiple access (CSMA) with collision avoidance (CA)
- Zigbee protocol is one realization of the IEEE 802.15.4 specification
- Physical layer (PHY), & part of MAC (media access control) with AES (advanced encryption standard) are incorporated in hardware.
- Globally unique address
  - 64 bit MAC address
  - 24 bit OUI, and 40 bit manufacturer assigned
  - additional 16 bit network address designating the current network

---
Wireless network - star

---
Node software
- At node power up
  - searches the medium for the presence of a network
  - if a network is found, the node checks the network identity
  - if it is a recognizable network, makes a request to join
- Micrcontrollers of the netowkr nodes have digitized sensor data
  - e.g., data is sampled at 1000 samples/second
  - Node uses a timer interrupt for ADC
  - Data packets size 80 bytes
  - 16 bytes are for a header specifying the type of data
  - 64 bytes of data

---
Co-ordinator software
- coordinator power up
  - checks the medium for networks
  - if its own network identity does not already exist, starts own network
  - after network has been started any recognizable node is allowed to join
- Coordinator is a state machine
  - States set by Software (Bluetooth/Zigbee) stack (interrupt driven)
  - States are polled for priority of action
  - Coordinator can also send data packets to the nodes

---
Pulse width modulation (PWM)
- Fixed clock rate, variable pulse width
  - Information encoded as pulse width
- Easy to decode
  - Estimate pulse width
  - Lowpass filter
- Poor error correction capability

---
End of Lecture