Inertial Sensors
Motion Sensing
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Accelerometers and Gyroscopes
- Acceleration sensing
- Angular velocity sensing

---
Accelerometers and Gyroscopes
- Inertial motion
- Do not depend on connection to a reference frame
  - “Tetherless”
- Suitable for ambulatory measurement

---
Accelerometers
- Measurement of acceleration
  - Force and mass: F=ma
- Acceleration due to gravity is always present on Earth
- Need to separate acceleration due to motion from gravity

---
Measurement of Acceleration

---
Principle of Equivalence
- From the point of view of a mass:
  - Acceleration due to gravity is indistinguishable from acceleration due to motion
- A mass in a gravitational field experiences a force in the same way as if the mass is moving with acceleration

---
Tilt measurement

---
Accelerometer axes

---
Tilt sensing with multi-axis accelerometer
- Tilt of the sensor with respect to the direction of acceleration
- Used in mobile devices, games, etc.

---
Gyroscope
- Spinning mass
- Spin, Precession, Nutation
- Gyroscopic moment
  - Moving particles in the rim of wheel
- Tilt wheel
  - Resisting force

---
Gyroscope

---
Gyroscope Principle

---
Disc gyroscope
mgr=%omega_s~%omega_p~I_s
- Mass, m
- Radius of disc, r
- Spin angular vel
- Precession angular vel
- Spin moment of inertia
mgr = %omega_s %omega_p I_s

---
Example
- Disc of mass: m=5kg
- Spin=12 rps
- Radius of spin gyration, r = 70mm
- Precession=0.5 rps
- Spin : ωs=2(3.14159)(12)=75.4 radians/s
- Precession: ωp=2(3.14159)(0.5)=3.14159 rad/s
- Moment of inertia:Is=(m)(r2)=0.0245 kg.m
- Gyroscopic force=ωsωpIs=5.8 Nm

---
Vibrating gyroscopes

---
Vibrating gyroscope – Coriolis force
- Force, F
- Angular Velocity of rotation/precession
- Linear velocity of oscillation
- Mass, m
F=-2 %omega_p v_osc m

---
End of Lecture