Radiation Thermometry
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Radiation Thermometry
- Non-linear sensors
  - Radiation Thermometer Example
- Digitization and digital sensors

---
Thermometry – thermal radiation
- Non-contact measurement - necessity and advantages
- Thermal radiation and temperature (steel)
  - Bright yellow: 2000 C
  - Bright red: 1500 C
  - Red-gray: 1000 C
  - Gray: 800 C
  - Blue: 575 C
  - Purple: 520 C
  - Brown: 480 C

---
Thermal Emission and Temperature – Planck’s Law
W( %lambda, T )= {2hc^2} over { %lambda ^5 left ( e^{hc / (%lambda k T)} right ) -1 }
Ref for graphs: T.K.Risch, 2015

---
Thermal Radiation – Wien’s law → peak radiation
W( %lambda, T )= C_1 over { %lambda ^5 left ( e^{C_2 / (%lambda T)} right ) -1 }
%lambda_{peak} = 2897 over T %mu m

---
Fractional Thermal Power

---
Stefan-Boltzman Law – radiation (absorbed/emitted)
- Integrating Wien’s equation can get total thermal power
  - integrate numerically
- Empirical formula by Stefan and Boltzman
- For black body, the emissivity is 1
- ‘A’ is a geometry factor
P_tot = A %epsilon %sigma T^4
P_{tot (blackbody)} = %sigma T^4
%sigma = 5.67037 Wm^-2 K^-4

---
Emissivity
- Radiated energy depends on surface properties, reflectivity
- Emissivity = Ratio of power emitted by a material to the power emitted by a perfect radiator (black body)
- Emissivity ranges from 0 to 1

---
Measuring thermal radiation
- Single wavelength measurement
- Two point measurement
- Multi-point spectrum measurement
  - Can estimate emissivity
- Measure Temperature rise due to absorbed energy
  - Thermocouple (thermopile)

---
Thermal Energy Measurement – PN jn voltage PTAT
V_BE = V_G0 ( 1-T over T_0 )+V_BE0( T over T_0 )-( nkT over q ) ln( T over T_0 )+kT over q ln( I_C over I_C0 )
%DELTA V_BE = kT over q ( I_C1 over I_C2 )

---
Thermal Energy Measurement – PN jn voltage PTAT
(Proportional To Absolute Temperature)
V_BE = V_G0 ( 1-T over T_0 )+V_BE0( T over T_0 )-( nkT over q ) ln( T over T_0 )+kT over q ln( I_C over I_C0 )
%DELTA V_BE = kT over q ( I_C1 over I_C2 )
- Semiconductor PN junction voltage depends on temperature (T) and current (I)
- Using a transistor with controlled collector current, and measuring the Base-Emitter voltage, we can calculate the junction temperature
- Sometimes, two transistors with Ic in a fixed ratio is used. The difference in VBE can be used.

---
Example of radiation thermometer

---
Calibration of temperature sensors
- Calibrate against a known sensor
- Calibration of conductive and radiative sensors
- Standard Black-body - cavity

---
Applications of radiation thermal sensors
- Single point measurement
- Infrared arrays/scanners for thermal photography
- Superimposition of thermal and visible light images
- Insulation testing of thermal vessels in power plants
- Insulation testing of buildings
- Mapping Heating and Energy loss in electronic and mechanical systems
- Human body temperature measurement
  - Use laser beam to show area of measurement

---
Measuring Human temperature
- Thermoregulation in animals and humans
  - Maintenance of core temperature
  - controlled by the hypothalamus
- Alteration in thermoregulation – fever
- Estimation of core body temperature
  - Sub-lingual, axillary fossa
  - Forehead – convenience
- Mass screening for individuals with fever

---
End of Lecture