Digital Sensors
Distance Sensing
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Distance sensing
- Magnetic sensing

---
Non-contact Distance Measurement - Optical
- Triangulation method
- Time of Flight (ToF) methods
  - Transit time measurement
  - Phase difference measurement

---
Triangulation method

---
Triangulation calculation
d over h = x_o over x_1 newline newline d= { x_o h} cdot {1 over x_1}

---
Sharp Sensor GP2Y0A21YK0F

---
Time of Flight methods
- Time difference between two pulses – transmitted and received
- Time-to-digital converters (TDC7201 )
  - Start and stop signals
  - Resolution 55 ps (0.000055 us)
- Time for light: 33 ps / cm

---
ToF LiDAR

---
Phase-change measurement
- Modulated light signal
- Phase difference between transmitted and received
- Example:
  - Frequency=60MHz
  - One cycle = 16.6 ns

---
Computational Delays in Digital Sensors
- Actual delay due to A/D and numerical calculations
- Repetition interval of calculations
  - Clock driven repetition
  - Take measurement
  - Perform calculation
  - Output numerical data
  - Repeat

---
Note on safety with lasers
- Lasers cause damage by heating
- NOHD=Nominal Ocular Hazard Distance
- Class 1: less than 39μW and/or enclosed
- Class 2: 0.99mW NOHD=7m
- Class 2M: safe up to 0.25s
- Class 3R: 4.99mW NOHD=16m
- Class 3B: 499.9mW NOHD=160m
- Class 4: over 500mW
  - 1W NOHD=224m
  - 10W NOHD=710m

---
Magnetic Sensing
- Hall effect: Potential difference in a current carrying conductor in a magnetic field
  - Electric potential is normal to Current and magnetic field
- Hall sensing is possible in three directions
- Applications
  - Rotation sensing
  - Magnetic field measurement

---
End of Lecture