Biopotential Electrodes
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Lecture - Outline
- Bioelectric measurement
  - Biopotential Measurement
  - Electrical Excitation
- Polarization and impedance
  - Implications for measurement
  - Frequency response
- Geometry considerations
  - Frequency response

---
Biopotentials
- Electrical potentials in excitable tissue
  - cardiac potentials – ECG
  - Brain potentials – EEG
  - Muscle and nerve – EMG, ENG
- Change in position and magnitude of charge separation (“dipole”)
- Generator potentials, action potentials, etc.

---
Measurement of biopotentials
- Measure the electrical field or potential at a point
- Conductive electrode placed in the tissue
- Record time-varying magnitude of potential
- Critical factors
  - Location of source
  - Orientation of nerve cells/muscle fibres along which dipole moves
  - Location and orientation of electrodes

---
Electrode Configuration for Biopotential Measurement
- Unipolar measurement
  - Measure potential at single point
  - Ground or Reference is an electrically inactive region
- Biopolar measurement
  - Differential measurement between two points
  - Ground or Reference at an inactive region
  - Differential Mode Measurement is signal
  - Common mode is noise

---
Measurement model
- Biological source – electrical source and source impedance
- Electrode-tissue interface
  - polarization potential
  - Electrode-tissue impedance
- Biopotential amplifier
  - Input impedance
    - Impedance between Differential inputs
    - Impedance between input and ground

---
Measuring Biopotentials
- Measured potential
  - Biological source
  - Half cell potential
  - Ion mobility across gradient
  - Electrode impedance Ohmic drop
- Vm(t)=Vb(t)+Vh+Vc(t)+VR(t)

---
Biopotential electrodes
- Electrodes have half-cell potential, ohmic potential drop, polarization potential
- Half-cell potentials w.r.t. hydrogen electrode
- Separation of ionic solutions
  - Nernst potential
{H_2 -> 2H^+ ~ + 2e}~~ drarrow { 0 V} newline {Al -> Al^+++ ~ + 3e}~~ drarrow {-1.7 V} newline { Cu -> Cu^++ ~ + 2e }~~ drarrow { +0.34 V } newline { Ag + Cl -> AgCl +e }~~ drarrow { 0.233 V }
V_C={RT} over { nF } log_e left ( { C_1 over C_ref } right )

---
Electrochemical Cell Potentials

---
Artifacts in Biopotential recording
- Change in activation – movement
- Polarization potentials
- Ag/AgCl Electrodes
- Movement artifacts
- Electrodes as filters

---
Measurement model

---
Electrode geometry and filtering – Bipolar electrodes
Size and separation of electrodes
e_S(t) = I_o over {4 %pi} left lbrace { 1 over {sqrt {(z-ut-w/2)^2 +d^2}} - 1 over {sqrt {(z-ut+w/2)^2 +d^2}} } right rbrace

---
Types of electrodes
- Surface electrodes
- Needle electrodes
- Concentric needle electrodes
- Fine wire electrodes

---
Stimulation electrodes
- Short-term and long term stimulation
- Charge accumulation
  - Charge balancing of electrodes

---
End of Lecture