Review
Suresh Devasahayam
Department of Bioengineering
Christian Medical College, Vellore

---
Ultrasound Measurement

---
Ultrasound Reflection Measurement

---
Ultrasound Instruments
%tau = 2d over c
- Time of echo:
- Attenuation:
- Automatic depth dependent gain compensation
%tau~ = ~2d over c
I_r over I_o~=~e^{- %mu (2d) }

---
Flow measurement
Transit time =
distance / (effective velocity in medium)

---
Doppler shift
- Source frequency fo
- Source-target velocity u
- Propagation in medium with velocity c
- Dopplet shift fd
{ f_d } over { f_o } = u over c

---
Flow Measurement

---
Dilution methods
C_i F + { dm} over {dt } = C_o F
F = { dm / dt } over {C_o -C_i}

---
Digital Measurement

---
Digital Temperature sensor - TMP100

---
Digitization and Quantization

---
Inertial Sensors

---
Measurement of Acceleration

---
Gyroscope Principle

---
Disc gyroscope
mgr=%omega_s~%omega_p~I_s
- Mass, m
- Radius of disc, r
- Spin angular vel
- Precession angular vel
- Spin moment of inertia
mgr = %omega_s %omega_p I_s

---
Vibrating gyroscope – Coriolis force
- Force, F
- Angular Velocity of rotation/precession
- Linear velocity of oscillation
- Mass, m
F=-2 %omega_p v_osc m

---
Distance Measurement

---
Triangulation calculation
d over h = x_o over x_1 newline newline d= { x_o h} cdot {1 over x_1}

---
ToF LiDAR

---
Radiation Thermometry

---
Stefan-Boltzman Law – radiation (absorbed/emitted)
- Integrating Wien’s equation can get total thermal power
  - integrate numerically
- Empirical formula by Stefan and Boltzman
- For black body, the emissivity is 1
- ‘A’ is a geometry factor
P_tot = A %epsilon %sigma T^4
P_{tot (blackbody)} = %sigma T^4
%sigma = 5.67037 Wm^-2 K^-4

---
Biopotential Electrodes

---
Measurement model

---
Photospectrometry

---
Absorption spectrum change of phenol red with pH

---
Examples requiring Design

---
1. Measuring eye-blink for noise removal
- Noise in EEG recording
- Remove noise by subtracting blink event-related potential
- Determine transfer relation between blink measurement and EEG measurement

---
2. Measuring eye-blink to use as control signal
- Locked-in patients – eye-blink under voluntary control
- Encode intention as sequence of eye-blinks

---
3. Electrogastrography
- Measure peristalsis
- Distinguish signal from movement noise

---
4. Measuring Blood flow in tissue
- Photoplethysmography
- Impedance plethysmography

---
5. Separating signal from noise
- Similar characteristics
  - ECG/EMG
  - EEG/EMG
- Different characteristics
  - ECG/respiration

---
Designing Measurement Systems
- Sensitivity
- Selectivity
  - Noise immunity
- Linearity
- Dynamic response
- Non-invasive
- Portability
  - Battery operation
  - Wireless data transfer