Making a voice coil:

Take a Ferrite ring of length=20mm, outer diameter=20mm, inner diameter=15mm.
Place it in a coil of wire with 20 turns; current through wire =1A.

Ferrite => Hc=60 Amp-turn/m, Br = 0.15 Weber/sq.m
Ferrite ring is saturated and fully magnetized.

R_m = H_c over B_m l_m over A_m = 400 left ( {0.02} over {137.5x10^-6} right ) = 58.2 x 10^3 Amp-turns/Weber

Pole piece: length = 20mm, diameter = 13mm. Fe permeability: %mu=6 x 10^-3

R_p = 1 over %mu l_p over A_p = 10^3 over 6 0.02 over { 530 x 10^-6 } = 6.3 x 10^3

Air gap:
R_g = 1 over %mu_o l_g over A_g = 1 over { 4 %pi 10^-7 } {2x10^-3} over { 880 * 10^-6 }=1800x10^3

Flux in the air gap:
B_g = H_c over { R_m + R_p + R_g } R_g = H_c x 0.965 = 58 Wb/m^2

Coil: 40 gauge (diameter 0.08 mm), 125 turns. Length of coil=10mm.

Diameter of coil = 14 x 10-3 m. Length of wire=1.75 m

Resistance of coil = 5.8 Ω

Inductance (iron core): L = %mu N^2 A over l= 6 x 10^-3 x 15625 x {154 x 10^-6} over {10 x 10^-3} = 1.44 H

Static case:

Excitation voltage = 6V
Current = 1.03 A
Force: F=BIl= 105N

Dynamic Case:

Excitation voltage is time varying: V(t)

Current: V( t ) = R~I( t )+L { dI(t) } over { dt }
 I( s ) = { V(s) } over { R+Ls } = {V( s )} over {Z_e( s )}

When coil is moving, EMF due to moving conductor in magnetic field:

V_b (s)=B_g l_c u(s)

V(s) = V_e(s) + V_b (s) newline ~~~~~~~~~~= {I(s)} {Z_e(s)} + B_g l_c u(s)

Velocity of movement can be determined from the mechanics:

F(t) = m dot u(t) + k_b u(t) + k_1 int u(t) dt newline u(s) = F(s)/[ms+k_b +k_1 /s] newline u(s) = {B_g l_c I(s)} over{ms+k_b +k_1 /s}
V(s) = V_e(s) + V_b (s)= {I(s)} {Z_e(s)} + I(s) {B_g ^2 l_c ^2} over {ms + k_b + k_1/s}
V( s )=I( s )[ Z_e(s)+Z_m(s) ]